## Slide 1: Performance Analysis with MARTE
Murray Woodside
Dept. of Systems and Computer Engineering
Carleton University, Ottawa, Canada
A presentation to OMG’s MARTE Information Day, Dec 12, 2007
  Concerns of Performance Analysis (PA)
  How MARTE supports PA
  Some examples from the document

## Slide 2: Concerns of Performance Analysis
Schedulability
Domain: control, robotics, monitors and alarms
safety critical
behaviour can be made to be deterministic
requirements are to meet hard deadlines
  (100% of responses<target)
Performance
Domain: service systems
  enterprise
  web
  best-effort networks
user can wait safely
behaviour is intrinsically non-deterministic
  execution demands
  data demands
measures and requirements are statistical, e.g.
  average response<target
  95% of responses<target

## Slide 3: A Simple but Typical Example
A web-based application
2 CPUs linked by a LAN
the application is integrated into the web server process

## Slide 4: An Interaction in the Example
processes
  thread pools
workload intensity
Steps in order
  host (execution) demands
  message sizes

## Slide 5: Challenges in Performance Analysis
stochastic models of behaviour are intrinsically complex
  simplified descriptions are needed for manageable effort
  e.g. mean, or mean and variance instead of probability distribution for host demand
information systems are evolving great complexity
  analysis must be approximate
assembly of services from components or other services
  flexible composition
specs of these systems are often incomplete
  it must be easy to supply defaults or approximations for missing detail (visible in alternative treatments of communications costs)

## Slide 6: There are Many Methods of Performance Analysis
Many PA methods:
Queueing networks
Layered Queueing Networks
Other kinds of Extended Queueing Networks
Petri Nets
Stochastic Activity Nets
Stochastic Process Algebras
Stochastic Automata
...and simulation languages
“Any”
design model
with
performance
annotations
“Any”
performance
model
Core
Scenario
Model
(CSM)
Performance
results and design
advice
Convert CSM to
this performance
model language
Extract C
SM
from this
design tool
Explore
solution
space
Feedback
A project of ours called PUMA integrates
many PA methods with annotated specifications
(ref: ACM WOSP 2005)
PUMA
operations

## Slide 7: How MARTE Supports Performance Analysis
Generic Quantitative Analysis Modeling (ch 15) supports both SA and PA
prefixes Ga, Sa, Pa.
Ga is used by Pa for
  Context,
  Workload,
  Scenario,
  Resources
Schedulability (ch 16) Performance (ch 17)

## Slide 8: Special Aspects of PA, compared to SA
are more in the quantities (NFPs) and how they are used, than in the stereotypes
  statistical rather than deterministic...
  difference in emphasis and detail
also, support for approximation and abstraction

## Slide 9: Statistical Quantities for Input to the Analysis
The most important difference in PA is the common use of statistical quantities
host demands (execution demand of a Step, in time units or cycles)
data sizes, for retrieval handling costs
message sizes, for network handling costs
probabilities of optional paths
loop counts for repeated operations
applied workload intensity:
  user population size
  user population external delay
  arrival rate

## Slide 10: Statistical Quantities for Output from Analysis
average, variance percentile or distribution of response time
average throughput of user requests and other messages
  database request rate
  I/O rate
average utilization of resources, or probability distribution of busy units
  buffers occupied
  busy threads
  probability a lock is in use

## Slide 11: Attributes that are used differently
e.g.: Workload Intensity
Open workload: an arrival stream with a rate (here: Poisson arrivals)
  <<GaWorkloadEvent>>{open(interArrT=(exp(17,ms)))}
    “open” is one of a set of choices; it is a function with one argument, the interarrival time.
    “exp( )” is a function with one argument, the mean
    “17,ms” is an NFP for the value of the mean
a periodic stream is also possible, but less common in these systems

## Slide 12: Workload Intensity (cont’d)
Closed Workload: a population making requests
  <<GaWorkloadEvent>>{closed(population=Nusers, extDelay=ThinkTime)}
    Nusers and ThinkTime are variables. For analysis Nusers should be an integer and ThinkTime, a time value
Workload Generator: a mechanism, usually expressed by a state machine, for generating the arrival events
  can be used to initiate particular sequences of sub-scenarios, with probabilities of next sub-scenario...
  e.g. browse buy exit

## Slide 13: PA Extensions to GQAM
<<Step>> is extended for additional properties:
  a Step may include three kinds of invoked behaviour, with invocation counts:
    an operation by a Component, called a ServiceDemand for a RequestedService
    an operation by another Scenario defined separately, called a BehaviourDemand
    an operation defined outside the UML specification, called an ExternalOperation (this has to be understood by the analysis environment)
    This supports modular specification, and complex services defined in other ways (e.g. not in UML)
A new <<ResourcePass>> Step subtype is added, to show a logical resource is passed to another process (e.g., passing a buffer)
A new <<RunTInstance>> resource type is added to explicitly and compactly identify a lifeline or swimlane with a deployed process instance (without explicit allocation submodel) (usability issue)

## Slide 14: Treatment of Communications
a message on a UML diagram is conveyed by some mechanism
  the runtime (between objects in Java)
  a middleware (e.g. CORBA, or a J2EE app server)
  the OS (e.g., by a pipe)
  a protocol layer (TCP)
for usability, it may or may not be desirable to show the mechanism explicitly in the UML
  perhaps, just indicate what is used
  or just annotate the total assumed overhead costs, to approximate the cost
Communications is modeled by a CommStep

## Slide 15: Support for Approximation/Abstraction: Communications
Five levels of abstraction
message between objects: no special cost
between nodes via OS: overhead/Byte on deployment
OR external operation (externalOpDemands) with more detail
by middleware defined by a StructuredClass (component model), with its own behaviour (servDemands)
by an arbitrary protocol with a separately defined behaviour (behaviorDemand, specifying a Scenario)

## Slide 16: Communications examples
<<PcommHost>>
LAN
{blockT = 10, us,
capacity = 100, Mb/s}
<<Phost>>
AppHost
{commTxOvh = (2, us)}
<<Phost>>
DBhost
database
webserver
<<PcommStep>>
msgSize = (4.5, KB),
behavDemand = parallelRead
behavCount=1}
<<PcommStep>>
{msgSize = (4.5, KB),
extOpDemand = network
extOpCount = 1}
<<PcommStep>>
{msgSize = (4.5, KB),
servDemand = conveyMsg
servCount = 1}
<<PcommStep>>
{msgSize = (4.5, KB)}
2:
4:
6:
8:
()
1:
()
3:
()
5:
7:
default
Middleware
<<Pservice>>
+conveyMsg()

## Slide 17: Communications example: default
database
webserver
<<PcommStep>>
msgSize = (4.5, KB),
conveyScenario = parallelRead}
<<PcommStep>>
{msgSize = (4.5, KB),
extService = network}
<<PcommStep>>
{msgSize = (4.5, KB),
conveyService = conveyMsg}
<<PaCommStep>>
{msgSize = (4.5, KB)}
2:
4:
6:
8:
()
1:
()
3:
()
5:
7:
the performance model uses the LAN characteristics to create a server submodel,
and the Hosts have overhead CPU demand parameters (not shown) which are added to the workloads at sender and receiver
<<GaCommHost>>
LAN
{blockT = (10, us),
capacity = (100, Mb/s)}
<<Phost>>
AppHost
{commTxOvh = (2, us)}
<<Phost>>
DBhost

## Slide 18: Communications example: External submodel
database
webserver
<<PcommStep>>
msgSize = (4.5, KB),
conveyScenario = parallelRead}
<<PcommStep>>
{msgSize = (4.5, KB),
extService = network}
<<PcommStep>>
{msgSize = (4.5, KB),
conveyService = conveyMsg}
<<PcommStep>>
{msgSize = (4.5, KB)}
2:
4:
6:
8:
()
1:
()
3:
()
5:
7:
“network” identifies a network submodel to the modeling tool, which inserts it into the final performance model, using the message size
Host overhead parameters are still used,governed by message size

## Slide 19: Communications example: Middleware Service
“Middleware” can be a structured class defining a subsystem
conveyMsg is an operation of that class
the PaRequestedService stereotype inherits from Step
it defines its own overheads or scenario, so default Host values of overhead are not used
database
webserver
<<PcommStep>>
msgSize = (4.5, KB),
conveyScenario = parallelRead}
<<PcommStep>>
{msgSize = (4.5, KB),
extService = network}
<<PcommStep>>
{msgSize = (4.5, KB),
conveyService = conveyMsg}
<<PcommStep>>
{msgSize = (4.5, KB)}
2:
4:
6:
8:
()
1:
()
3:
()
5:
7:
Middleware
<<PaRequestService>>
+conveyMsg()

## Slide 20: Communications example: Scenario
behavDemand = parallelRead
[ ]
par
SendMW
RcvMW1
RcvMW2
Sender
Receiver1
Receiver2
2:
6:
10:
3:
5:
7:
9:
1:
4:
8:
[ ]
par
arbitrarily complex sequences of behaviour
  good for protocol detail executed at both ends and at servers
entities must represent deployed processes (no dynamic binding )
multiple deliveries in this case must be interpreted:
  receiver behaviour is nested into the Receiver step(s)

## Slide 21: Other kinds of Analysis
Power analysis could closely follow performance, with energy demands as well as time demands
Memory seems to have the same possibility, adding data sizes to objects and/or operations
Reliability: failure and repair events can be modeled with MARTE annotations on failure/repair state machines. In principle there seems to be no barrier.

## Slide 22: Example of a Performance Model: an electronic bookstore (TPC-W). Deployment Diagram

## Slide 23: TPC-W Behaviour: One Scenario (GetHomePage)
One of 16 scenarios defined in the benchmark spec (by the Transaction Processing Council)
Context parameters declare some variables,
some are declared in place
closed workload
required and calculated variables
msgSize expression
repeated Step
probability of alt
external operation for imageserver file retrieval
Figure 17.14
1
4
5
7
3
8
6
2

## Slide 24: TPC-W GetHomePage Scenario Expanded: Top of Diagram
One of 16 scenarios defined in the benchmark spec (by the Transaction Processing Council)
Context parameters declare some variables,
some are declared in place
closed workload
required and calculated variables
msgSize expression
repeated Step
probability of alt
external operation for imageserver file retrieval
Figure 17.14
1
4
5
7
3
8
6
2

## Slide 25: TPC-W Expanded: Bottom of Diagram
1
4
5
7
3
8
6
2

## Slide 26: Queueing Model of 10 scenarios
annotation is total
  host demand
  per user response
all single servers
WebserverCPU runs the webserver and imageserver processes
WebserverCPU
(3.7 ms)
User
(ThinkTime)
FinancialServer
(23.3 ms)
DatabaseCPU
(10.3 ms)
{Nusers}

## Slide 27: Layered Queueing Model of the GetHomePage scenario

## Slide 28: LQN for 10 scenarios
Although this model is complex, solutions are fast (seconds)
the 10 scenarios as operations
actions they invoke at webserver
actions at DataBase, imageServer and financialServer

## Slide 29: Solutions of the LQN
Response time
Throughput
huge improvement found with redesign
  read-only cache for promotion