## Slide 1: Initial Submission SWRADIO/03-01-01 to PIM and PSM for SWRADIO Components SWRADIO/02-06-02 RFP
Jerry Bickle
Raytheon
+1-260-429-6280
Gerald_L_Bickle@Raytheon.com
Francois-Xavier LEBAS
THALES Communications France
+33.(0)1.41.30.24.20
francois-xavier.lebas@fr.thalesgroup.com
Dr. Jeffrey Smith
Mercury Computer Systems
+1-978-256-0052
jesmith@mc.com
Software Radio Submission Email: srsupport@yahoogroups.com

## Slide 2: Contents
Introduction
  Submitters and Supporters
  Background
  SDR Stakes
  Goals
Approach
  Key Principles
  Communication Channel
  Facilities
  Use Cases
Summary
  Status

## Slide 3: Submitters and Supporters
Submitters
  Mercury Computer Systems
  Raytheon Company
  THALES Communications France
Supporters
  Carleton University
  General Dynamics Decision Systems
  Fraunhofer FOKUS
  L-3 Communications Analytics Corporation
  MITRE
  Harris
  BAE Systems
  Rockwell Collins

## Slide 4: Background
A Software Defined Radio (SDR) is a wireless communication system (low-rate single channel mobile phones to high-capability multi-channel radios), in which the particular communication and transmission characteristics are realized through specialized software running on flexible signal processing hardware.
Notes: Also, it would be great value if the implementation of each of these communication schemes would be portable such that it could be loaded onto a standards-compliant, device made by any manufacturer.

## Slide 5: SDR Stakes
Functional Stakes
  Concurrent waveforms within the same radio set
  Increased support to digitized communications
    bridging, routing,
    end-to-end QoS
  Enhanced versatile Security
    remote (re)configuration (OTAR...)
  Reconfiguration & Download
    remote firmware and software updates, new services
  Ease Monitoring & Diagnostics
Industrial Stakes
  Enable Technology Insertion
  Software Reuse and Portability
  Improve Engineering Process
Notes: Last bullet – In the past, more of the waveform functionality had to be implemented by hardware components.

## Slide 6: Goals
To define a set of facilities within a software radio domain that promotes:
  Seamless interoperability between distributed components, each realized with different technologies & techniques
  Portability of SDR applications across different platforms
  Forward compatibility for upgrades
  Improved efficiency of SDR applications development

## Slide 7: Approach
Key Principles
Communication Channel
Facilities
Use Cases

## Slide 8: Key Principles
PIM has been primarily structured as a set of facilities each addressing a key aspect of SDR
PIM uses a well-defined set of modeling conventions
  Naming conventions
  Modeling conventions
  Subset of UML notation (notation is mainly based on UML 1.4 and UML 2.0 proposed by the U2Partners)
  Specific semantics of this notation in the context of this PIM
Submission conforms to MDA
  PIM defining general concepts for SDR
  PIM can be transformed to different component platforms
    CORBA-PSM, Java-PSM, etc.
Submission compatible with existing OMG standards
  MOF
  UML

## Slide 9: Approach
Key Principles
Communication Channel
Facilities
Use Cases

## Slide 10: Communication Channel
A Communication Channel is that part of a SDR which provides the direct means to communicate information between parties
The typical Communication Channel consists of
  RF Channel
    the analog elements transitioning signals between baseband and the ether
  Processing Channel
    providing the waveform and signal processing capabilities
  Security Channel
    providing encryption / decryption of the signal
  I/O Channel
    connecting the SDR to users / other equipment
Notes: Communication channel concepts presented herein are covered by a U.S. patent application by Raytheon Company. If adopted as part of an OMG standard, Raytheon will license the technology on a no fee basis for use in implementing the standard.

## Slide 11: Communication Channel
Notes: Customer View
Many times they must buy new hardware to switch or upgrade their waveforms.Users of communication equipment cannot switch between waveforms or upgrade their current waveforms as quickly and as easily as needed.
This makes switching or upgrading waveforms to bemore expensive, more difficult, and more time consuming
System view
  Equipment designs have a short life span before they need to be replaced by new designs to support additional features/waveforms.
    This makes designs and manufacturing more expensive
    Note: for some commodities and market conditions this may not be a desirable approach.

## Slide 12: RF Channel

## Slide 13: Processing Channel

## Slide 14: Security Channel

## Slide 15: I/O Channel
Notes:     Waveform developer view
    This makes waveform design and implementation to be less expensive.
    This will lead to radios that interoperate.

## Slide 16: Communication Equipment

## Slide 17: Approach
Key Principles
Communication Channel
Facilities
Use Cases

## Slide 18: What is a facility?
A “Facility” is a service that can be shared by applications and that supports domain-specific functions.
“Facilities” refers to a set of services related a certain aspect of the system.
Services/components:
  Behavior provided by a part of the system
  Shared by several waveforms
  Specific to the SDR domain

## Slide 19: Facilities
Communication Channel
Facility 1
Facility
L
. . .
Component 1
Component 2
Component
N
. . .
Component-to-component interaction
Instantiated Channel (WF components)-to-facility interaction
Device 1
Device
M
Component-to-device control
Rcv
channel in
Rcv
channel out
RF
User
data
RF
Xmit
channel out
User
data
Xmit
channel in
. . .
Notes: Def. of SDR: Wireless communication characteristics are realized in software running on flexible hardware.
Software model: Waveform is top level application, an assembly of components; Component: a software unit controlling a hardware device have standard interfaces (for interoperability) an standard mappings (for portability). Facility: a domain specific service share by waveforms (e.g. modem, link layer, media access control, network management).
Hardware model: hardware devices such as Digital signal Processor, Field Programmable Gate Arrays, General Purpose Processors, RF components.
Channel: Waveform and corresponding hardware devices, translate digital data source into a RF signal and/or vice versa.
Implementation framework: operating system (e.g. RTOS); middleware (e.g. CORBA, communication with and between components).

## Slide 20: SDR Facilities
RF/IF Facilities
Waveform Processing Facilities
Networking Facilities
Security Facilities
Radio Control Facilities
Common Waveform Facilities
Common Radio Facilities
I/O Facilities

## Slide 21: RF/IF Facilities
Definition
  These facilities define the functionality to convert the digitized signal into a propagating RF wave, and conversely, to convert a propagating RF wave into a digitized signal for processing.
Examples of RF Facilities
  Filters/Interface Cancellation
  Frequency Tuning
  Up/Down Conversion
  Analog Digital Conversion
  Gain Control
  Synthesizer

## Slide 22: Waveform Processing Facilities
Definition
  These facilities define the functionality to create waveform packets and synchronization data out of the input data streams and vice versa according to the waveform specifications.
Examples of Waveform Processing Facilities
  MAC Facilities
    Components providing the media access control behavior of a waveform
    High correlation with SCA’s MAC API (Appendix F)
  Link Layer Facilities
    Components providing the link layer behavior of a waveform
    High correlation with SCA’s LLC API (Appendix G)
  Physical Facilities
    Modulate/Demodulate
Notes: Includes En/decoding also at any layer

## Slide 23: Networking Facilities
Definition
  These facilities define the functionality for network management and network behavior for a waveform
Examples of Networking Facilities
  Routing
  Network Management
    Conceptual equivalence with Internet network management.

## Slide 24: Security Facilities
Definition
  These facilities define the functionality for communications security and transmission security.
Examples of Security facilities
  Encryption/Decryption
  Transmission Security
  Algorithms
  Keys
Notes: For example in the military, the comsec facility typically stays between the red and the black side. Concepts relate to the SCA Security Supplment

## Slide 25: Radio Control Facilities
Definition
  These facilities define the functionality to configure, get status, and control the radio domain.
Examples of Radio Control Facilities
  Alarms and Alerts
  Communication Channel Control
  Radio Control

## Slide 26: Common Waveform Facilities
Definition
  These facilities define the set of services that are specific to waveform processing within the radio and associated with many waveforms.
Examples of Waveform Common Facilities
  Scanner Facility
  Retransmission Facility
  Time Facility
  Cosite Facility

## Slide 27: Common Radio Facilities
Definition
  These facilities define the set of services that all components within the radio can used.
Examples of Common Radio Facilities
  Lightweight Log
  Lightweight Naming Service
  Lightweight Event service
  Lightweight CCM
  File Facility
  Basic SDR Component Interfaces
Notes: Some of these services are being standardized within the OMG by other submissions: Lightweight Services, Deployment & Configuration, Lightweight Log FTF, and Lightweight CCM. Concepts derived from the SCA

## Slide 28: I/O Facilities
Definition
  These facilities defines the functionality for base band I/O such as serial and audio devices.
Examples of I/O Facilities
  Common I/O Facilities
    Digital I/O
    I/O control
  Audio Facilities
    Microphone, Speaker, CODEC
  Data Facilities
    Serial
Notes: Codec – encoding and decoding for audio

## Slide 29: Approach
Key Principles
Communication Channel
Facilities
Use Cases

## Slide 30: Use Cases
Use Cases are used to flush out the definitions and to validate the SDR Facilities
Realization of the use cases using the SDR Facilities are captured in the form of sequence diagrams
The use case model (composed of use case packages, use case diagrams, and individual use case descriptions) will be provided in the final submission (work in progress)
In this Initial Submission, Use Cases are provided to OMG community as typical examples (to be discussed) of radio system and radio set operations.
In later submissions, Use Cases realization will be mapped onto SDR Facilities as a preliminary proof-of-concept.

## Slide 31: Summary
Overall Goal:
  Definition of a platform-independent model for Software Defined Radio
Initial Submission
  Follows MDA: PIM
  Communication Channel Concept
  SDR Facilities
Preview Partial revised Submission March presentation
Revised Submission planned for June
  PSM
  Completion of Use Cases and Facilities
Feedback is appreciated