## Slide 1: Waveform Characteristics
Jeff Smith
March 26, 2003

## Slide 2: Motivation for “Softer” Waveform Generation Technology & Reusable Components
Waveform developer
JTeL
Government
SIGINT
Spec developer
Spec implementer
Forward engineering waveform from parts, separation of concerns
Repository and verification of waveform parts
Common understanding, non-redundancy, reduced costs
Working platform to apply constrained search to waveform classification
Check on services, use case identification and reduction and concise uniform description of waveform requirements
Reusable waveform components and capture of waveform design options, parameters and trades
If you are a
You get

## Slide 3: Characteristic Conceptualization
Characterize waveforms into waveform attributes such that one could describe a waveform by combinations of types and parameters:
Unfolded table dimension = x1* x2 * x3*…* xN
Waveforms can be thought of as unique paths in this 2-space
Maximum size is product of columns
Air interface (x1) | Packet content (x2) | Connection type (x3) | Access mode (x4) | Signal type (x5) | …
FDMA | voice | networking | hopping | analog | 
CDMA | data | point-to-point | non-hopping | digital | 
TDMA |  | broadcasting | direct sequence |  | 
DAMA |  |  |  |  | 
Push-to-talk |  |  |  |  | 
Trunked |  |  |  |  | 
… |  |  |  |  | 
A
B

## Slide 4: Waveform Configuration in N Dimensions
x5 = signal type
analog
digital
x2 = packet
content
CDMA
FDMA
TDMA
data
voice
DAMA
x1 = air interface
consistent attributes
inconsistent attributes
x2 = packet
content
CDMA
FDMA
TDMA
data
voice
DAMA
x1 = air interface
analog
digital
with analog data, QPSK
modulation cannot be used

## Slide 5: Next 3 dimensions
x6 = source
coding
x4 = spectral mask
x7 = channel coding
x1 = TDMA
x2 = digital
xN = data

## Slide 6: Larger View of Waveform Characteristics Ontology Used at OMG
Signal: SWRI classification (see http://www.ece.neu.edu/~mbicer/Mobilecom/doc.html)
Packet content: voice (analog & digital), data (digital), voice & data
Connection type: networking, point-to-point, broadcast, multicast
Switching type: circuit, packet
LOS: yes, beyond
Access mode: push to talk, trunked, DAMA,TDMA,CDMA (direct sequence, multi-carrier), CSMA, FDMA
Security: transmission, communication, none
Spectral mask: center frequency, instantaneous frequency, bandwidth, power
Channel coding: convolutional, turbo, Reed Solomon, CRC, none
Routing: RF packets, IO packets
Source coding: yes, no
Channel estimation: adaptive, trained, blind, none
Power control: open loop, closed loop, none
* Need to check against JTRS waveforms (http://jtrs.army.mil) and revise

## Slide 7: FM3TR Example
FM3TR Data Transmission Mode
FM3TR Voice Transmission Mode

## Slide 8: Each Point in 2-Space Has OSI Level Meaning
Characteristic Type
Characteristic Parameter
Characteristics can be realized in 7 OSI layers
Layers of characteristics realized as SCA components
Layer parts gathered from multiple waveforms & reused to compose a waveform protocol stack
Component layering transparent to the SCA CF
Deal with only the waveform channel but extendable to info proc and IO channels
Info proc
channels
Waveform channels
IO channels
From École de technologie supérieure, Jean Belzile
OSI Level
Notes: Reuse layer parts gathered from multiple waveforms
  Classify/standardize parts of parts of waveforms (see Jean Belzile, http://groups/.yahoo.com/srradio)
Protocol translator between 3-d cells
Reuse physical interfaces for multiple freqs
Jean has continued our work, dividing by OSI layers

## Slide 9: Waveform Characteristics and their Relation to the OSI Layer Model

## Slide 10
the ability to set and read performance criteria – QOS
the ability to set and read a baud rate – timing
the ability to set and read a radiation pattern – transducter response
then the ability to set and read a power setting – Amplification
…

## Slide 11: Physical layer class diagram

## Slide 12: Data link layer class diagram

## Slide 13: Characteristic Constraints can Partitioned for Parallel Optimization
A waveform space of N dimensions can be represented as, x1,x2, … ,xN}, where the set of N vectors need to be determined according to the constraint set A waveform may be represented as p(x1(3), x2 (5), x3 (2), …, xN (6)) = true, s.t. constraints e.g. dead-end, aggregation, etc.
The optimal waveform is found by choosing the parameters that minimize the cost function J( .) s.t. such that:
opt = {arg min J( ) |, arg min J( ) |},
P1 P2 Pm
s.t. Ki are independent, mutually exclusive & cover all constraints, partitions Pn are therefore mutually exclusive where,
J( ) |J(Pj) |j
j=1
m

## Slide 14: Reformulation of Problem…
1. The relationship between every possible building block can be seen as a mesh network, where a connected line means an “allowed path” between two nodes
A/D
Access mode
All
All
A
D
A
A
D
D
TDMA
FDMA
CDMA
TDMA
FDMA
Info
Sec
no
Info
Sec
yes
2. By choosing different root nodes, the mesh network can be viewed as a different tree
D
x1
x2
x3
x4
xn
P1
P2

## Slide 15: Spec and Implementation Generation
Requirements
Waveform Specification
Waveform Implementation
Other Alternatives
Other Alternatives
Formally Validatable
Automated Process
Automated Process
3. Application dependent constraint analysis
  Check feasibility of each application constraint
  Create search tree given application priorities
4. Automated optimization
  Use high-performance search technique to find optimal waveform specification that meets application constraints

## Slide 16: Waveform Generation Technology Next Steps
Refine and publish N-space, testing against JTRS legacy waveforms
Input for a bounded set of use-cases for the OMG SWRadio spec (check on services)
Apply search and constraints against refined waveform characteristics
  Build constraints as predicates over characteristics composing the points in waveform configuration space
    Output power, baud rate, bit error rate, frame error rate
  Use high-performance search techniques to identify viable candidates