## Slide 1: Information Assurance Challenges in Army Tactical Networks
David Carman, Principal Cryptographic Engineer, McAfee Research
Prepared through collaborative participation in the Communications and Networks Consortium sponsored by the U. S. Army Research Laboratory under the Collaborative Technology Alliance Program, Cooperative Agreement DAAD19-01-2-0011. The U. S. Government is authorized to reproduce and distribute reprints for Government purposes notwithstanding any copyright notation thereon. The views and conclusions contained in this document are those of the authors and should not be interpreted as representing the official policies, either expressed or implied, of the Army Research Laboratory or the U. S. Government.

## Slide 2: Information Assurance Challenges
Focus of This Talk
  Key Management
  Intrusion Detection
Other Important Research Challenges
  Routing Security
    How do we make a MANET routing protocol, that inherently needs cooperation, resistant to subversion by non-cooperating nodes?
  Trust Management
    How do we efficiently establish and maintain trust relationships in a MANET when our trusted third-parties (e.g., Certifying Authorities) are distant or unreachable?
  Secure and Survivable Network Servers
    How do we efficiently preserve low-latency availability of network services while simultaneously restricting access to only legitimate clients?
  Efficient, Robust Message Authentication
    How do we preserve the authenticity of messages in a manner that is highly-efficient in terms of both communications and computations?

## Slide 3: Key Management Research Challenges

## Slide 4: Tactical Environment
Ad Hoc
  Nodes will not know a priori who they will interact with on the battlefield
Mobile
  Links will appear and fail often in normal operations
Close to the enemy
  Nodes subject to physical attack and compromise
Multi-hop data routing
  Many network services will require multi-hop messaging
    Examples: Auto-configuration, QoS, DNS, etc.

## Slide 5: High-Level Key Management Requirements
Limit Data Protected By Each Key
  Limit amount of data revealed by a node compromise
  Each unique communicating pair has its own key
  Forwards and backwards secrecy
  Separate link and network layer security associations
Revocation for detected compromise
Key updating for undetected compromise
Group key management
KAB
KBC
KCD
KAD
A
B
C
D

## Slide 6: Group Key Management Requirements
Each Unique Group Needs a Unique Key
Link Layer Keying
  One key used to encrypt
  and authenticate link-layer
  broadcasts such as routing
  messages
Network Layer Keying
  One key used to encrypt
  and authenticated network-
  layer multicast messages
Carol
Dave
Eva
Frank
Gail
Bob
Alice
Carol
Dave
Eva
Frank
Bob
Alice

## Slide 7: Constraints to Implementing Security
Limited computational capability
  Slows public key operations
Limited battery energy
  Not a universal constraint
  Communications consumes more energy than computations
Limited communications capability
  Suboptimal antennas
  Lower-rate anti-jam wireless links
  Shared media access control layer
  Shared network (other traffic besides security  )
    Additional security information (e.g., key management messages, authentication tags, IVs) further congests network
  Low effective channel rate  slows key establishment

## Slide 8: Conventional Approaches
Interactive Key Management Protocols
  IKE/IKEv2  HAIPE
    Use Diffie-Hellman + digital signatures or other authentication
    Requires four or more messages to be exchanged
    Elliptic-curve cryptography reduces message sizes
  Transport Layer Security (TLS) / Secure Sockets Layer (SSL)
    Requires four or more messages to be exchanged
Non-interactive Key Management Protocols
  Pre-positioned secret keys
    “Master” network-wide keys are vulnerable to single node compromise
  Pre-positioned public keys
    Unable to handle new nodes

## Slide 9: Problem Scenarios
Scenarios where traditional key management techniques do not work well or do not exist:
1. Large Initial Latency for Multi-hop Messages
2. Highly-Mobile Link-Layer Key Management
3. Link-Layer Broadcast

## Slide 10: Large Initial Latency for Multi-hop Messages
1. Alice generates and sends IKE_SA_INIT msg
2. Karen generates and sends IKE_SA_INIT msg
3. Alice generates and sends IKE_AUTH msg
4. Karen generates and sends IKE_AUTH msg
5. Alice encrypts data message and sends to Karen
Alice
Bob
Carol
Dave
Eva
Frank
Gail
Henry
Isabel
John
Karen
Scenario 1: Alice wants to send an encrypted and authenticated message to Karen, but must first use IKEv2 to negotiate a security association

## Slide 11: Impact of Link-Layer Acknowledgements
100 link-layer messages must be sent in precise order!
Alice
Bob
Carol
Dave
Eva
Frank
Gail
Henry
Isabel
John
Karen
1. Alice generates and sends IKE_SA_INIT msg
2. Karen generates and sends IKE_SA_INIT msg
3. Alice generates and sends IKE_AUTH msg
4. Karen generates and sends IKE_AUTH msg
It’s more complicated than that when link-layer ACKs are considered…
5. Alice encrypts data message and sends to Karen

## Slide 12: Link-Layer Keying Before Network-Layer Keying
140 total link-layer messages must be sent!
Alice
Bob
Carol
Dave
Eva
Frank
Gail
Henry
Isabel
John
Karen
1. Alice generates and sends IKE_SA_INIT msg
2. Karen generates and sends IKE_SA_INIT msg
3. Alice generates and sends IKE_AUTH msg
4. Karen generates and sends IKE_AUTH msg
It’s even more complicated when link-layer security is considered…
5. Alice encrypts data message and sends to Karen
0. More messages needed for interactive key management to generate link-layer security associations
Factor in Mobility
Factor in Intermittent Connectivity

## Slide 13: Alternative: Identity-Based Cryptography
3. Alice sends data message to Karen via Bob, Carol, Dave, etc.
Alice
Bob
Carol
Dave
Eva
Frank
Gail
Henry
Isabel
John
Karen
Only 20 link-layer messages needed!
Latency significantly reduced:
  Time required to send 20 vs. 100 link-layer messages
Network overhead reduced:
  Eliminates 80 link-layer messages for each new pairwise network interaction
2. Alice computes link-layer pairwise keys based on Bob’s identity and encrypts and authenticates link-layer message
1. Alice computes network-layer pairwise keys based on Karen’s identity and encrypts and authenticates network-layer data message

## Slide 14: Identity-Based Public Key Cryptography
Public key technique where a node’s public key is derived from its unique identity (ID)
  “Jay Gowens @ ARL” is hashed to create Jay’s public key
Corresponding private keys are generated by a system authority and distributed to nodes
Advantages
  No certificates, the public keys are “self-authenticating”
  No certificate distribution
  No certificate servers / repositories
IDA, xA
A

## Slide 15: Identity-Based Key Management
Pre-deployment
Key Authority loads:
Pairwise Keying
A
B
C
IDA
IDB
KAB
KAB
Group Keying
KAB
KAC
KAC
KAB
KGroupA
IDB
IDA
IDC
IDA
A generates:
A computes
wrapping keys
B computes
unwrapping key
C computes
unwrapping key
IDA, xA
IDB, xB
IDC, xC
A
xA
B
xB
B
xB
A
xA
C
xC

## Slide 16: Non-Interactive Keying Elements
Public key distribution provided by identity-based cryptography
Forward secrecy provided
via ephemeral (time-limited)
identity-based keys for
pre-defined validity periods
  Ex: “Jay Gowens @ ARL 051704 1600-2000Z”
Key freshness using available unique values (e.g. SPIs, key IDs, counters)
IDA
IDB
KAB(t)
KAB(t)
A
xA(t)
B
xB(t)

## Slide 17: Link-Layer Pairwise Keying & Mobility
Bob
Carol
Dave
Eva
Frank
Gail
Conventional Interactive Keying Scenario
Alice receives a beacon/hello message from a node.
Alice exchanges four key management messages with each new node she encounters before she can send/receive a link-layer data message (e.g., routing).
Problem - If Alice is moving fast enough, she will only have time to exchange key management messages, not data; potentially not even completing the key establishment at all.
Alice
Alice
Alice
Alice
Alice
Alice
Alice

## Slide 18: Alternative for High Mobility Keying
Bob
Carol
Dave
Eva
Frank
Gail
Identity-based Pairwise Keying Scenario
Alice receives a beacon/hello message from a node.
Alice computes link-layer pairwise keys based on node’s identity and encrypts and authenticates link-layer message.
Alice sends link-layer message.
Alice
Alice
Alice
Alice
Alice
Alice
Alice

## Slide 19: Problem: Link-Layer Group Keying & Mobility
Alice
Problem 1:
When Alice comes within bidirectional communications range of Bob, Bob’s group must establish a new group key to preserve secrecy of past data
Bob
Dave
Eva
Frank
Alice
Problem 2:
When Alice leaves bidirectional communications range of Bob, Bob’s group must again establish a new group key to preserve secrecy of future data
Alice

## Slide 20: A Link-Layer Group Keying Solution
Bob
Dave
Eva
Frank
Adding Alice to the Group Scenario
Alice sends a beacon/hello message to Bob
Bob performs a known one-way function on the group key, incrementing the group key ID
Bob computes the pairwise key between him and Alice using the time and Alice’s identity
Bob wraps the new group key using the pairwise key and transmits it to Alice
Subsequent link-layer messages will contain the new group key ID, which Dave, Eva and Frank can derive using the known one-way function
Alice
Alice

## Slide 21: A Link-Layer Group Keying Solution (2)
Bob
Dave
Eva
Frank
Removing Alice from the Group Scenario
Bob no longer hears a beacon/hello message from Alice
Bob generates an entirely new group key, incrementing the group key ID
Bob wraps the new group key using the previously computed identity-based pairwise keys for Dave, Eva, and Frank and transmits them to each
Subsequent link-layer messages will contain the new group key ID, for which Dave, Eva and Frank will now have the corresponding group key
Alice
Alice
Potential problem: communications are “blocked” during re-keying.

## Slide 22: Additional Challenges
Transition to Battlefield
  Identity-based cryptography too immature for military use?
    Maurer-Yacobi
    Weil and Tate pairings
    Random key predistribution
  No ready alternatives that satisfy high assurance needs under battlefield constraints
Key Management for “Large” Dynamic Groups
  Combining hierarchical and identity-based techniques____
Component subgroup
Group leader

## Slide 23: Intrusion Detection Challenges

## Slide 24: Intrusion Detection Goals
Provide effective and efficient intrusion detection in fully-mobile, ad hoc, self-configuring, multi-hop, wireless networks
Provide intrusion detection coverage for all traffic
Address broad spectrum of attacks
  Conventional “wired” attacks
  “Wired” attacks in a wireless, ad hoc world
  Brand new MANET-specific attacks
    Routing and auto-configuration protocols inherently vulnerable
    Widely distributed port scans and DDoS attacks
Minimize bandwidth utilization
Detection performance must degrade slowly due to failed/compromised components

## Slide 25: Intrusion Detection Constraints
No concentration points where traffic can be analyzed
  Intrusion data must be shared with other nodes
Limited communications capability  low effective channel rate
  Limits how much raw intrusion detection data can be shared
    Degrades attack recognition performance
  Slows dissemination of intrusion detection data
    Slows attack recognition
Intermittent connectivity caused by mobility/noisy channels
  Degrades attack recognition performance due to partial data
Limited energy, CPU processing, and storage resources
  Limits attack recognition capability
Highly dynamic networks with mobile nodes AND mobile infrastructure (routing, security, configuration)
  Architecture must be dynamic and perform hand-offs

## Slide 26: Intrusion Detection Constraints (2)
“Hidden terminal” effects, channel contention, and confidentiality mechanisms
  Degrades promiscuous monitoring
Normal user and network behaviors not easily characterized due to mobility of networks and the full spectrum of tactical missions
  Cannot solely rely on anomaly detection
Forward-deployed nodes prone to enemy capture
  Intrusion detection architecture must be tolerant to Byzantine nodes
Analyst intervention during tactical operations limited
  Automated intrusion response mechanisms needed
Varying resources available in heterogeneous networks
Wireless communications medium susceptible to eavesdropping, jamming/interference, and denial-of-service attacks
Network addresses do not always reflect location (physical or hierarchical)
Cannot rely on centralized network or security services

## Slide 27: State of Research and Key Challenges
Intrusion Detection in MANETs research relatively young
  Long-standing research focused on fixed, wireline networks
  Emerging research in MANETs focuses primarily on routing misbehavior
  Detection techniques reported are either statistical anomaly detection or simplistic promiscuous routing monitoring
  Key research from Zhang and Lee proposes distributed, cooperative network intrusion detection
Key unresolved research issues
  Consumption of computational and communication resources
  Effects of intermittent connectivity and high mobility
  Comprehensive intrusion detection (not just routing misbehavior)
  Attack recognition using partial and aggregated data, and of complex multi-stage attacks
  Cross-layer designs
  Efficacy of training and relying on statistical anomaly detection

## Slide 28: A Cooperative Detection Hierarchy
Events
Aggregated
Data
Correlation Results,
(Further) Aggregated Data
(Further) Correlated Results,
(Even Further) Aggregated Data
Mobile Ad Hoc Nodes
Cooperatively
Determined
Level 1
Clusterheads
1
1
1
1
2
3
Signature Updates,
Request for Detailed Data
Signature Updates,
Request for Detailed Data

## Slide 29: Cooperative Detection Hierarchy
Attack detection and correlation occur at the lowest level at which aggregated data is sufficient for an accurate decision
    May occur at a single node at the bottom, e.g., for an unambiguous, single-packet attack such as “ping of death”
    May occur incrementally at multiple levels (tentative decisions) using increasingly complete sets of data
    Benefits:
      Reduces detection latency
      Reduces amount of detection data that must be transmitted from child to parent
Non-Hierarchical interactions also permitted, e.g., to correlate attacks through chained-connections

## Slide 30: Cooperative Intrusion Detection Roles
Data Source
  Acquires raw detection data
Detector
  Performs attack recognition
Alert Correlator
  Identify patterns in detected attacks
Aggregator
  Consolidate detection data from other nodes
1
2
Alert Correlator
Detector
Aggregator
Data Source
Detector
Aggregator
Data
Source
Data
Source
Detector
Data Source

## Slide 31: Attack Recognition Techniques
Signature-Based Detection
  Matches network data to stored signatures
  Widely-used operational technique
  Does not address unknown attacks
Statistical Anomaly Detection
  Measures resource allocation overuse
  Requires little bandwidth, no signature files/updates
  Developing normative profiles via training difficult for wide spectrum of MANET uses
Specification-Based Detection
  Compares behavior of components with specification of correct component behavior
  Can recognize unknown attacks; requires no training or signature files
  Developing error-free specifications for complex behaviors is tedious and difficult

## Slide 32: Intrusion Detection Strategies
Area Detection
  Detector obtains data via promiscuous eavesdropping
Synergistic Detection
  Other nodes directly report detection data to detector
En route Detection
  Node that is on a route between two communicating end points acts as detector
Self Detection
  Each node monitors packets it originates or consumes. Also encompasses host-based intrusion detection.

## Slide 33: Questions?