## Slide 1: Revised Submission SWRADIO/03-05-01 to PIM and PSM for SWRADIO Components SWRADIO/02-06-02 RFP
Jerry Bickle
Raytheon
+1-260-429-6280
Gerald_L_Bickle@Raytheon.com
Francois-Xavier LEBAS
THALES Communications France
+33.(0)1.41.30.24.20
francois-xavier.lebas@fr.thalesgroup.com
Dr. Jeffrey Smith
Mercury Computer Systems
+1-978-256-0052
jesmith@mc.com
Software Radio Submission Email: srsupport@yahoogroups.com

## Slide 2: Contents
Introduction
  Submitters and Supporters
  Background
  SDR Stakes
  Goals
Approach
  Use Cases
  Key Principles
  UML Profile for SDR
  Facilities
Summary
  Status

## Slide 3: Submitters and Supporters
Submitters
  Mercury Computer Systems
  Raytheon Company
  THALES Communications
Supporters
  BAE Systems
  Boeing
  Carleton University
  ETS
  Fraunhofer FOKUS
  General Dynamics
    Decision Systems
  Harris
  Intel
Note: Submitters and Supporters are also members of the Software Defined Radio Forum (SDRF) which are working on common SDR APIs.
  - ISR Technologies
  - L-3 Communications
    Analytics Corporation
  - MITRE
  - MobileSmarts, Inc
  - Rockwell Collins
  - SCA Technica
  - Spectrum Signal Processing Inc.

## Slide 4: Background
A Software Defined Radio (SDR) is a wireless communication system (low-rate single channel mobile phones to high-capability multi-channel radios), in which the particular communication and transmission characteristics are realized through specialized software running on flexible signal processing hardware.
Notes: Also, it would be great value if the implementation of each of these communication schemes would be portable such that it could be loaded onto a standards-compliant, device made by any manufacturer.

## Slide 5: SDR Stakes
Functional Stakes
  Concurrent waveforms within the same radio set
  Increased support to digitized communications
    bridging, routing,
    end-to-end QoS
  Enhanced versatile Security
    remote (re)configuration (OTAR...)
  Reconfiguration & Download
    remote firmware and software updates, new services
  Ease Monitoring & Diagnostics
Industrial Stakes
  Enable Technology Insertion
  Software Reuse and Portability
  Improve Engineering Process
Notes: Last bullet – In the past, more of the waveform functionality had to be implemented by hardware components.

## Slide 6: Goals
To define a set of Facilities within a software radio domain that promotes:
  Seamless interoperability between distributed components, each realized with different technologies & techniques
  Portability of SDR applications across different platforms
  Forward compatibility for upgrades
  Improved efficiency of SDR applications development

## Slide 7: Approach
Use Cases
Key Principles
UML Profile for SDR
Facilities

## Slide 8: Use Cases
Use Cases are used to flush out the definitions and to validate the Facilities
Realization of the use cases using the Facilities are captured in the form of sequence diagrams
The use case model is composed of use case packages, use case diagrams, and individual use case descriptions.
In this Revised Submission, Use Cases are provided to OMG community as typical cases of radio system and radio set operations.
In Final submission, Use Cases realization will be mapped onto Facilities as a preliminary proof-of-concept.

## Slide 9: Use Cases Categories
  Are described in a separate document:
    swradio/2003-05-02
  150 Use Cases
    Transmit/Receive (22)
      FM3TR, W-CDMA, HF 4285
    Control (13)
      Radioset Control
      Waveform Control
    Administration (63)
      (Re)configuration
      Diagnostic
      Fault Management
    Security (32)
      Key management

## Slide 10: Use Case Examples

## Slide 11: Use Case Example
Use Case Identifier: - Power-up and Initialize
Description: An Actor such as the Operator, Maintainer, etc., applies power to the Radio Set which then performs activities such as:
  1. BIT/diagnostics
  2. Bus enumeration,
  3. Communication network configuration
  4. I/O configuration
  5. Device initialization
The Radio Set optionally loads default waveform(s) (see note 1).
External Actors: Operator, Maintainer
Related Use Cases:
Precondition: The power is off to the Radio Set (see note 2). The Operator has authorization to use the Radio Set.
Triggering event:
Notes:       Comments:
Note 1: Default waveform boot-up is optionally a function of the Radio Set, or it may be partitioned out to an application element such as the GUI.
Note 2: The previous shutdown of the Radio Set was performed in an orderly way as per the "Shutdown" Use Case. In other cases of more abrupt power-down, separate use case functionality would apply.

## Slide 12: Use Case Example, cont’d
Main Flow:
    1 The Operator applies prime power to the Radio Set.
    2a The Radio Set successfully completes power-up BIT per the Initiate System BIT use case, and the Radio Set reports status (e.g. OE is operational).
    3a The Operator acknowledges the startup of the OE and begins authorized use of the Radio Set.
    4a The Radio Set presents the options for the Operator to Configure Radio, Run Diagnostics, Receive/Transmit, etc. [end of case]
  Resulting event:
  Postcondition:
    The Radio Set is ready to be configured and has optionally established default communications path(s).
  Alternatives:
    2b The Radio Set fails power-up BIT with a critical failure.
        1 [end of case]
    2c The Radio Set fails power-up BIT with a non-critical failure.
        1 The Radio Set reports failure [continue at 3].
    3b The Operator finds that the operational status is a degraded mode which would not provide sufficient capability for current needs.
    1 The Operator selects the shutdown option. [end of case]

## Slide 13: Use Case Realization Example #1

## Slide 14: Use Case Realization Example #2

## Slide 15: Approach
Use Cases
Key Principles
UML Profile for SDR
Facilities

## Slide 16: Key Principles
Waveform Characterization
ISO/OSI Conformance
Design Principles

## Slide 17: Waveform Generation Technology & Reusable Components
Waveform developer
JTeL
Government
SIGINT
Spec Dev
Spec Implementer
Forward engineering waveform from parts, separation of concerns
Repository and verification of waveform parts
Common understanding, non-redundancy, less money
Working platform to apply constrained search to waveform classification
Check on services, use case identification and reduction and concise uniform description of waveform requirements
Reusable waveform components and capture of waveform design options, parameters and trades
If you are a:
You get:

## Slide 18: Characteristic Conceptualization
Characterize waveforms into waveform attributes such that one could describe a waveform by combinations of types and parameters:
Unfolded table dimension = x1* x2 * x3*…* xN
Waveforms can be thought of as unique paths in this 2-space
Maximum size is cross-product of columns
Air interface (x1=5) | Packet content (x2=2) | Connection type (x3=3) | Access mode (x4=3) | Signal type (x5=2) | …
FDMA | voice | networking | hopping | analog | 
CDMA | data | point-to-point | non-hopping | digital | 
TDMA |  | broadcasting | direct sequence |  | 
DAMA |  |  |  |  | 
Push-to-talk |  |  |  |  | 
Trunked |  |  |  |  | 
… |  |  |  |  | 
… |  |  |  |  | 
A
B

## Slide 19: Need for Waveform Characterization
A large number of use cases exist
We established a systematic process to define and characterize the use cases
Broad participation in use cases generation including submitters, contributors and other participants
The characterization of the use cases used to drive the standardization of the software radio facilities and use-case closure

## Slide 20: Waveform Characterization
A comprehensive set of waveforms and studied
WF characteristic model boundaries were chosen such that a representative set of waveforms can be covered
Characteristic attributes were also checked to be independent from each other
Each characterization can further be represented in one or more OSI layers

## Slide 21: FM3TR Example
FM3TR Data Transmission Mode
FM3TR Voice Transmission Mode

## Slide 22: ISO/OSI Conformance
OSI layered architecture was adapted to SDR
At least one layer of the OSI model can be associated with each waveform characteristic
Waveform and OSI model are viewed as orthogonal functionalities
Cross-referencing with waveform characteristics was made to show how two models fit together
The layered model was shown to be able to support primary waveform requirements
Component layering transparent to the SCA CF
Layers of characteristics realized as SCA components

## Slide 23: OSI Model
Info proc
channels
Waveform channels
IO channels
From École de technologie supérieure, Jean Belzile

## Slide 24: Design Principles
PIM has been primarily structured as a set of facilities each addressing a key aspect of SDR
PIM uses a well-defined set of modeling conventions
  Naming conventions
  Modeling conventions
  Subset of UML notation (notation is mainly based on UML 1.4 and UML 2.0 proposed by the U2Partners)
Submission conforms to MDA
  PIM defining general concepts for SDR
  PIM can be transformed to different component platforms
    CORBA-PSM, Java-PSM, etc.
Submission compatible with existing OMG standards
  MOF
  UML

## Slide 25: Approach
Use Cases
Key Principles
UML Profile for SDR
Facilities

## Slide 26: UML Profile for SDR Domain
  Stereotypes enable modeling and building of SDR applications.
    Communication Channels
    Communication Devices
    Standardization of property names helps ensure portability of waveforms. For example:
      Initialize Property – Has to be initialized upon startup/setup
      Configure Property – Configurable after startup
  Relationships capture the roles of the relationships and their constraints.
Notes: Communication channel concepts presented herein are covered by a U.S. patent application by Raytheon Company. If adopted as part of an OMG standard, Raytheon will license the technology on a no fee basis for use in implementing the standard.

## Slide 27: Communication Channel
A Communication Channel is that part of a SDR which provides the direct means to communicate information between parties
A typical Communication Channel abstraction consists of :
  RF Channel
    the analog elements transitioning signals between baseband and the ether
  Processing Channel
    providing the waveform and signal processing capabilities
  Security Channel
    providing encryption / decryption of the signal
  I/O Channel
    connecting the SDR to users / other equipment
Notes: Communication channel concepts presented herein are covered by a U.S. patent application by Raytheon Company. If adopted as part of an OMG standard, Raytheon will license the technology on a no fee basis for use in implementing the standard.

## Slide 28: Communication Channel
Notes: Customer View
Many times they must buy new hardware to switch or upgrade their waveforms.Users of communication equipment cannot switch between waveforms or upgrade their current waveforms as quickly and as easily as needed.
This makes switching or upgrading waveforms to bemore expensive, more difficult, and more time consuming
System view
  Equipment designs have a short life span before they need to be replaced by new designs to support additional features/waveforms.
    This makes designs and manufacturing more expensive
    Note: for some commodities and market conditions this may not be a desirable approach.

## Slide 29: RF Channel

## Slide 30: Processing Channel

## Slide 31: Security Channel

## Slide 32: I/O Channel
Notes:     Waveform developer view
    This makes waveform design and implementation to be less expensive.
    This will lead to radios that interoperate.

## Slide 33: Communication Equipment

## Slide 34: Approach
Use Cases
Key Principles
UML Profile for SDR
Facilities

## Slide 35: What is a facility?
A “Facility” is a domain-specific service used by applications
“Facilities” refers to a related set of services, e.g.
  Behavior provided by a part of the system
  Shared by several waveforms
  Specific to the SDR domain

## Slide 36: Facilities
Communication Channel
Facility 1
Facility
L
. . .
Component 1
Component 2
Component
N
. . .
Component-to-component interaction
Instantiated Channel (WF components)-to-facility interaction
Device 1
Device
M
Component-to-device control
Rcv
channel in
Rcv
channel out
RF
User
data
RF
Xmit
channel out
User
data
Xmit
channel in
. . .
Notes: Def. of SDR: Wireless communication characteristics are realized in software running on flexible hardware.
Software model: Waveform is top level application, an assembly of components; Component: a software unit controlling a hardware device have standard interfaces (for interoperability) an standard mappings (for portability). Facility: a domain specific service share by waveforms (e.g. modem, link layer, media access control, network management).
Hardware model: hardware devices such as Digital signal Processor, Field Programmable Gate Arrays, General Purpose Processors, RF components.
Channel: Waveform and corresponding hardware devices, translate digital data source into a RF signal and/or vice versa.
Implementation framework: operating system (e.g. RTOS); middleware (e.g. CORBA, communication with and between components).

## Slide 37: SDR Facilities
RF/IF Facilities
Waveform Processing Facilities
Networking Facilities
Security Facilities
Radio Control Facilities
Common Waveform Facilities
Common Radio Facilities
I/O Facilities

## Slide 38: RF/IF Facilities
Definition
  These facilities define the functionality to convert the digitized signal into a propagating RF wave, and conversely, to convert a propagating RF wave into a digitized signal for processing.
Examples of RF Facilities
  Filters/Interface Cancellation
  Frequency Tuning
  Up/Down Conversion
  Analog Digital Conversion
  Gain Control
  Synthesizer

## Slide 39: Waveform Processing Facilities
Definition
  These facilities define the functionality to create waveform packets and synchronization data out of the input data streams and vice versa according to the waveform specifications.
OSI conformance study will be mapped onto Waveform Processing Facilities
Examples of Waveform Processing Facilities
  MAC Facilities
    Components providing the media access control behavior of a waveform
  Link Layer Facilities
    Components providing the link layer behavior of a waveform
  Physical Facilities
    Modulate/Demodulate
Notes: Includes En/decoding also at any layer

## Slide 40: Networking Facilities
Definition
  These facilities define the functionality for network management and network behavior for a waveform
Examples of Networking Facilities
  Routing
  Network Management
    Conceptual equivalence with Internet network management.
  Radio specific retransmission and bridging

## Slide 41: Security Facilities
Definition
  These facilities define the functionality for communications security and transmission security.
Examples of Security facilities
  Encryption/Decryption
  Transmission Security
  Key Management (OTAR,OTAZ …)
Notes: For example in the military, the comsec facility typically stays between the red and the black side. Concepts relate to the SCA Security Supplment

## Slide 42: Radio Control Facilities
Definition
  These facilities define the functionality to configure, get status, and control the radio domain.
Examples of Radio Control Facilities
  Alarms and Alerts
  Communication Channel Control
  Push To Talk

## Slide 43: Common Waveform Facilities
Definition
  These facilities define the set of services that are specific to waveform processing within the radio and associated with many waveforms.
Examples of Waveform Common Facilities
  Scanner Facility
  Synchronization Facility
  Cosite Facility

## Slide 44: Common Radio Facilities
Definition
  These facilities define the set of services that all components within the radio can used.
Examples of Common Radio Facilities
  File Facility
  Basic SDR Component Interfaces
Notes: Some of these services are being standardized within the OMG by other submissions: Lightweight Services, Deployment & Configuration, Lightweight Log FTF, and Lightweight CCM. Concepts derived from the SCA

## Slide 45: I/O Facilities
Definition
  These facilities defines the functionality for base band I/O such as serial and audio devices.
Examples of I/O Facilities
  Common I/O Facilities
    Digital I/O
    I/O control
  Audio Facilities
    Microphone, Speaker, CODEC
  Data Facilities
    Serial
Notes: Codec – encoding and decoding for audio

## Slide 46: Summary
Overall Goal:
  Definition of a platform-independent model for Software Defined Radio
Revised Submission Achievements
  Use Cases completed
  Facilities defined
  Waveform characterization performed for use cases closure
Final Submission planned for September
  Use Cases realization
  Completion of Facilities
Feedback is appreciated