## Slide 1: Achieving Coalition C2 Interoperability Through Software Defined Radios

## Slide 2: Contributors
Dr. David Murotake Software Radio Architect Mercury Computer Systems, Inc.
dmurotake@mc.com
Mr. Craig Lund
CTO
Mercury Computer Systems, Inc. clund@mc.com
Dr. Jeffrey Smith Software Radio Program Lead Mercury Computer Systems, Inc. jesmith@mc.com
978-967-1760
Mr. Richard D. Hinman
Air Force Research Lab
Information Directorate/IFGC
Richard.Hinman@rl.af.mil
Mr. E. Kenneth Hong Fong CTO Systems Architecture OSD (AT&L) IO
The Pentagon 3D1073
ekenneth.hongfong@osd.mil
703-695-0472

## Slide 3: Challenges
The flexibility inherent of software defined radio may be the enabler for true military coalition C2 tactical interoperability.
Commercial and/or military products must coalesce around an agreed upon set of standards and interfaces if individual national systems are to be interoperable.
Multiple commercial and military standards committees address only portions of the interoperability challenge.
Our task is to understand how such standards will integrate into a cohesive communications system to deliver interoperability and how you can validate with respect to standards.
Need Proof of Concept systems that converge US JTRS, UK Bowman/PDRS and other important national players’ systems.

## Slide 4: Methodology
Learn by creating a releasable, reference, open source, proof-of-concept and demonstration.
Demonstrate a US JTRS radio user discovering and communicating with a node in an independent radio network (as may be deployed by a coalition partner).
Populate the proof-of-concept team with experts drawn from both real world radio developers, military operators and standards activities.
Verify that a system built from this collection of standards is interoperable and practical to integrate and deploy.

## Slide 5: Four Communities
Coalition tactical command & control
Software radio infrastructure
Waveform implementation
Standards and acquisition management/policy bodies

## Slide 6: Strawman Scenario
Consider an American tank that sees a coalition partner’s tank on a nearby hill. The tanks are likely on distinct nation-oriented defense networks. How does the American tank crew use a radio to spontaneously invite the coalition tank crew to lunch?
Sure, which bunker and what time?
Would you like to meet for lunch?

## Slide 7: Strawman Elements
6. Content (lunch?)
2. Discovery (linking) waveform
5. Communications waveform
4. Networking protocols
3. Identification process
1. C4I information (registry database)
Need coalition waveform demonstration, incorporating elements that will leverage standards, communication, networking and modeling investments.

## Slide 8: 1. C4I Database
Basic information is required before the communications negotiation begins.
  Sender’s identification information
  Security parameters
  Waveform parameters
This information comes from the C4I system.
  The sending tank might already have this information stored locally; or
  The sending tank might issue a real-time query into the C4I network.
Standards for how to transfer command and control parameters for SDR required – will investigate ICS derivative
  Minimum C2 interfaces/behavior for POC goals. Can solicit partner if we take broader C2 course.
Notes: Radio problem is no longer just a radio technology problem. We need to know something of the information environment and a priori info that surrounds radios

## Slide 9: Why ICS (Incident Command System)?
Proven, efficient method used since 1990s including 9-11 disaster response
Designed for use by multiple agency types and echelons
  Unified command/control
  Federal, State, Local, NGOs
  Civil and military
  Ability to leverage commercial standards, devices & infrastructure
Well documented, open source information on interfaces, behavior, forms
  http://www.fema.gov/emi/is195.htm
  Easy to model
  Information available to all countries and organizations
Highly scalable
  Early response
  Expansion/Contraction
  Demobilization
Greater acceptance by the international community
  Widespread reluctance to adopt existing US military C4I models (many issues)
  More likely to draw widespread support in many parts of the world because of focus on emergency response
Extensible to coalition warfare
Ideal for homeland defense

## Slide 10: 2. Linking Waveform
In a hostile signals environment some parameters cannot be known in advance.
Receiving tank must discover sending tank’s unexpected attempt to initiate dialog.
Existing standards in this domain include ALE for HF.
Identified no discovery/link waveform examples in WDL or in C that conform to the SCA model.
Notes: Radios can shift their parameters almost instantly and go from an optimized configuration for just establishing the link to a configuration for secure and efficient bulk information transfer

## Slide 11: Linking Waveform Summary
Modify existing linking protocol stack from MIL-STD-188-141 (HF-ALE)
Use FM3TR physical layer for VHF-UHF (CPFSK)
Mature HF-ALE software radio implementations are available as code sources (RL/IFGA), but not SCA. Can we re-use and re-deploy?
Can be used as a proposed link establishment method for FM3TR nets in future US-NATO dialog
Sender
Xmits
Send IFF interrogation, encrypted Link (ID) over all freqs
Receiver listens
For ID
For each valid receipt, send IFF response, ID, signal strength
Sender selects best channel based on ID & signal strength

## Slide 12: 3. Identification Process
A process is required to identify the intended recipient by:
  Geographic location,
  Call sign,
  Type/kind,
  By-product of an IFF subsystem,
  Etc.
ID process involves interaction with the C4I system and emits parameters used by the linking waveform.

## Slide 13: 4. Networking Protocols
Strawman uses a TCP/IP stack to “simulate” whatever wireless IP protocol ultimately emerges.
Future over-the-air demo could substitute streamlined, wireless, defense-oriented version of IP.

## Slide 14: 5. Communications Waveform
FM3TR baseline. ALE derivative will be inserted at FM3TR MAC layer using separate waveforms for discovery and communication.
Mercury has leveraged code base from successful US-UK-GE FM3TR (demo) to develop SE spec set and SCA-compliant waveform implementation.
Sound Capture and stream
Sound Reproduction
FM3TR Waveform Generation
Waveform Acq. and Data recovery
Frequency hopping Modulator
Frequency hopping Demodulator
Up Converter
Down Converter
T/R Switch
CVSD Vocoder
CVSD Vocoder
Multimedia H/W
Posix
Posix
Programmable Card
Channel simulation / RF Hardware
MIC
Speaker
Initial Prototype Module implementations
Future Enhancements
CORBA, SCA
CORBA, SCA

## Slide 15: FM3TR Summary
Future Multiband Multimode Modular Tactical Radio – “to ensure interoperability of software radios”
  Multi-national digital communications waveform
  Real-time, digital, frequency hopping
  AFRL has C code for CPUs &
  VHDL for FPGAs
Investigate availability &
applicability of AFRL WDL
waveform & process for
FM3TR (see backup)
FM3TR enhancements
for real world
Frequency Range
30-400 MHz
250 Hops/sec
Type
CPFSK
Rate
25 kb/sec
Index
0.5
Tx Spurious Emission

-75 dBm
Rx Image Rejection

-80 dBm
10 mW Tx
Power
Performance
Specification
Modulation
Hop Rate

## Slide 16: Green Tank, Blue Tank Communication
1. Shared a priori to engagement (mandatory):
  Frequency Scan List
  Communications waveform (e.g. FM3TR)
  ALE-derivative protocol
  IFF transponder code
  Network access and transmission security code
  Coalition ID code
  Coalition order of battle (OB)
Caller
Receiver
2/3. Discovery based interrogations (optional):
  Coalition OB information (Echelon/nationality, task force or strike team assignment)
  Resource capability summary
  Mission objective, clearance and priority
6. Inquiry (mandatory):
  Would you like to meet for lunch?
“Would you like to meet for lunch?”
2/3. Discovery based interrogations (mandatory):
  Identity based on Coalition ID code OR IFF transponder code and correct location/time

## Slide 17: Green Tank, Blue Tank Messaging
Secure automatic linking call + IFF interrogation
Secure automatic linking response + IFF reply
Discovery: I am a US Abrams attached to TF Green at [location]
Discovery: I am a French Leopard attached to Strike Team Blue at [location]
Inquiry: Would you like to meet for lunch?
Reply: Yes, your bunker or mine? Do you like quiche?
Reply: Your bunker is fine. Real tank crews don’t eat quiche.
Reply: Stand by for coded instructions for passage of lines
through our defensive screen using code X-ray…
Reply: Ready to decode X-ray
Coded transmission: Passage of lines information

## Slide 18: Strawman Functional Diagram
US Tank
Coalition Tank
Command & Control Functionality
IP Network
Channel
Simulation
Channel
Simulation
Comm.
waveform
Linking
waveform
SCA Core Framework
C4I Database
User
Interface
Comm.
waveform
Linking
waveform
SCA Core Framework
Foreign C4I Database
User
Interface
Notes: Only need small amount of C2 data
We will focus our attention on interfaces and behaviors and consulting
POC will not be a real working C2 system

## Slide 19: A model-based implementation because…
Contemporary software standards and reference architectures are expressed as models.
It is possible to generate much code directly from a model:
  Deployable systems are generally written from scratch and difficult to verify against original specifications,
  State-of-the-art has not yet caught up with efficient model generated code and code is not WDL
We must develop models where models do not exist and our resulting system’s reuse is more likely in the definition and test domain (as opposed to deployment).

## Slide 20: Vertical Architectural Layered View
CORBA ORB
OS that supports
SCA Application Environment Profile (AEP)
Applications (Radio/Comm Waveforms in WDL & Procedural Languages)
& Tools
Core Framework
Device Drivers
C2 Models
Networking/Linking (including Crypto)

## Slide 21: 4-Layer Meta-data Architecture
StockQuote(“Sunbeam Harvesters”, 98.77)
StockQuote(“Ace Taxi Cab Ltd”, 12.32)
Record(“StockQuote”,
[Field(“company”, String),
Field(“price”, FixedPoint)])
MetaClass(“Record”,
[MetaAttr(“name”, String),
MetaAttr(“fields”, List<“Field”>)]
MetaClass(“Field”, …)
MetaClass(“Class”)
M0
M1
M2
M3
info
model
meta-
model
meta-meta
model (MOF)

## Slide 22: SCA Example
M0
M1
M2
M3
info
model
meta-
model
meta-meta
model (MOF)
struct ProducerLogRecordType {
string producerId;
string producerName;
LogLevelType level;
string logData;
};

## Slide 23: Horizontal Modeling Layers & Standards
CORBA
POSIX compatible OS
specs implementation
SCA FM3TR implementation in
WDLs, Java, C, C++, …
XML + Languages
C/C++
& Assembly
ICS
ALE (including Crypto)
UML
UML
Semant
ics
MOF
M0
M1
M2
M3

## Slide 24: Waveform Development Environments
Communication service and protocol in waveform textual descriptions
Foresight’s or Racal’s WDL, Vanu’s RDL, or network layer functions in SIMULINK/MATLAB
Not MDA or SCA compliant.
Commercial
Ptolemy,
SystemView,
Foresight,
COSSAP,
GEDAE,
ISI,
SPW,
UML CASE
…
C4ISR
CADM,
DAFT,
JCAPS,
MRT,
CMMS,
JMAAT
…
Gudaitis/
Hinman

## Slide 25: Modeling Issues
Convergence of C4ISR Framework & AF C2 Enterprise Reference Architecture w/UML & SCA
  C2 nodes connected by CII Enterprise vs SDR node CORBA SW bus
  C4ISR Framework includes process model
  C4ISR Zachman-based Framework includes domain mandatory views
    Drill 4 dimensions of arch integration (National, Theater, CJTF, Tactical) and 3 architectural perspectives (operational, systems and technical)
  But not OMG standard (not UML or SCA)
Agreement on command & control model and network architecture, e.g., ICS
Alignment of evolving platform independent software radio behavior and platform specific models and WDL tools & library standards

## Slide 26: Summary
Need to develop a coalition interoperability demonstration, performing discovery, ID and communication over independent networks.
Must leverage standards, communication, networking and modeling investments, “give-back” to currently involved standards communities and consult to new C4I communities.
Cooperation needed with appropriate contractors and agencies to leverage investment and expertise.
Can map to broad applications e.g. emergency broadcast and data casting (see backup), terrorism and natural disaster recovery, etc. based on government feedback.
Will serve to prove multi-national interoperability concepts.

## Slide 27: Backup Material

## Slide 28: ATLANTIC PAW (APAW) 23 Oct 2001
Richard D. Hinman
Air Force Research Lab
Information Directorate/IFGC
525 Brooks Road
Rome, New York, USA
+1 (315) 330-3616
email: Richard.Hinman@rl.af.mil

## Slide 29
BACKGROUND
Phase 1 (FM3TR) completed:
  last meeting: 10-12/11/99 at Pforzheim (GE)
  successful GE/UK/US software radio interoperability demonstration
Phase 2 (APAW)
  MOU signed Sept 2000
  2nd TG meeting 15-17/05/01 at Charleston, USA

## Slide 30
Phase 1 - SUMMARY
Implementation/verification of real interoperable waveforms on different National Hardware platforms can be achived within rapid time frames
Essential collaborative demonstration on the road to an international Software Radio concept
Demonstrated the FM3TR technical concept.
Provided a firm foundation of proven systems for Phase 2 APAW and the definition of future common waveforms.

## Slide 31
APAW
Advanced Transmission Language and Allocation of New Technology for International Communications and the Proliferation of Allied Waveforms

## Slide 32
APAW OBJECTIVE
To enable interoperability of multinational wireless communications assets for combined operations.
To support portability of waveforms onto independent radio hardware by the definition and development of a common waveform description open standard.

## Slide 33
MIL-STD
STANAG’s
etc.
MW
SW
HW
Target Platform
System Engineering &
Software Engineering
Target
Platform
SW Code
Load SW
Code
MW
SW
HW
Demonstrable System
Target
Platform
SW Code
Test
NOTIONAL WAVEFORM IMPLEMENTATION

## Slide 34
MIL-STD
STANAG’s
etc.
WDL
Description
MW
SW
HW
Target Platform
Conversion
Process
Conversion
Process
Target
Platform
SW Code
Load SW
Code
MW
SW
HW
Demonstrable System
Target
Platform
SW Code
Test
APAW Decomposition of Development Process

## Slide 35
Scope of Work and Workshare
Six Tasks
Waveform Description Standard:
  Define the waveform description standard. (UK Lead)
  Define waveform parameter database and structure. (US Lead)
Utilizing the waveform description standard:
  Describe the FM3TR enhanced waveform. (FR Lead)
  Describe the SATURN legacy waveform. (GE Lead)
Using the agreed common description of the FM3TR and the SATURN waveforms, implement them onto national platforms. (GE Lead)
Demonstrate compatibility between national platforms and a SATURN legacy radio. (FR Lead)
Multinational demonstration. (US Lead)
Continue update and maintenance of the waveform database and structure. (UK Lead)

## Slide 36
NATIONAL PROGRAM - STATUS
FR
GE
UK
US

## Slide 37: FR STATUS
Joint FR/GE MMR Advanced Development Model radio program continuing:
  2000 - 2003
Software Study:
  Define a software architecture that enables Waveform portability (2001-2002)
  Implement this architecture on several demonstrators and check the portability (2002-2003)

## Slide 38: GE STATUS
Joint FR/GE MMR Advanced Development Model radio program continuing:
  2000 - 2003
Evaluation of candidate high data rate waveforms for interoperability continuing:
  Preliminary results presented at May 2001 TG

## Slide 39: UK STATUS
Phase 1, Programmable Digital Radio (PDR) Complete: WDL products offered to TG for APAW support
Phase 2, PDR Begun:
  Refine WDL:
    Specification for Object Library Functions and Services, Waveform Description Script, associated API’s to enable OEM ‘Interpreter’
  Implement: FM3TR, SATURN, UHF Wideband Waveform

## Slide 40: US STATUS
Study of commercial & open source based WDL options nearly complete (Emergent)
US comments on proposed UK WDL provided: At PDR review June 2001& PDR review Aug 2001
Contract for WDL prototyping awarded 19 Sep 2001
Development of hardware testbed (SoRDS) to verify WDL concept nearing completion (Dec 2001)
  FM3TR waveform implementation nearing completion
  SATURN waveform software support secured (MITRE)
AFRL Technical support to OUSD C3I office for planned UK-US JTRS/BOWMAN interoperability program:
  WDL likely to be used for software waveforms

## Slide 41: Emergency Broadcast & Data-casting (Arlan Pool – Mercury)

## Slide 42: Digital TV Services
Better Pictures
...HDTV...
WXYZ
More Programs
...Multicast...
New Services
...Data...
video
video
TEXT
audio 1
video
audio 2
PGM GD
video
video
video
video
19.4 Mbps

## Slide 43: FCC DTV Mandate
Experimental
stations on-air
Top 4 networks
Top 10 markets
(14% U.S. HH)
All
stations
First commercial
DTV stations
Top 4 networks
Top 30 markets
(53% U.S. HH)
All commercial
stations
End NTSC
broadcasts?
97
98
99
00
01
02
03
04
05
06
There are 1600 broadcasters in the U.S.
210 DTV Stations on-air Today

## Slide 44: Data and Video Distribution at Emergency Site
Potential uses:
  Broadcast of data communications to assist in an emergency management situation
    Limited existing communications infrastructure
    Natural disasters
      Earthquakes
      Hurricanes & weather
    Terrorism recovery efforts
      WTC recovery effort
    Humanitarian & Peace-keeping Missions
      Refugee management

## Slide 45: System Concept
Transmitter
DTV in a Box
Creation &
Server
Live Video,
Sattelite video &
Data feed
Power
Generator

## Slide 46: Capabilities
Video/Audio broadcasting
  Live video from site, downlink from satellite or tape
Capability to broadcast a website to a local computer system
  DTV Data-casting at up to 19.39 Mbit/sec bandwidth
  Ability to constantly update
Ability to encrypt data and/or video stream for communications to trusted devices
  Leverage broadcast “Conditional Access” capability
Capability to support multiple modulation schemes to meet situational requirements

## Slide 47: ICS Overview (DRAFT) An Open-Architecture, Scalable Command and Control Model for Multi-Agency Joint Civil/Military Operations Dr. D. Murotake Mercury Computer Systems, Inc.
http://www.fema.gov/emi/is195.htm

## Slide 48: Incident Command System (ICS) Candidate C4I Model can be extended to accommodate homeland defense and multi-national coalition operations
Command & control model in use by FEMA, FBI, DoD, states and local emergency response agencies
Designed for efficiency and scalability (early response, expansion, contraction, demobilization)
Used since 1990’s for disaster relief, firefighting, HAZMAT cleanup, search & rescue
Designed for multi-agency C3 including joint civil and military operations.
Well-suited for scalable, multi-national coalition operations
Incident Command
Operations Section
Combat Ops Branch
Southern Division
Reconnaissance Group
Northern Division
Main Battle Group
FR Armor Strike Team 14
USA Task Force 1-70
Blue Tank
Green Tank
Disaster Relief Branch
Law Enforcement Branch
Planning Section
Fin/Admin Section
Logistics Section

## Slide 49: ICS Scalable Command Function
The ICS Command Function provides a unified command structure, and can employ the most highly qualified individuals and resources from participating agencies.
The ICS permits ad-hoc formation of a command and control kernel during first response, scales gracefully as additional agencies and their resources join the organization, and offers excellent procedures for scale-down and demobilization.
First Response
ICS Command Function
“Full-up” Incident Response
ICS Command Function

## Slide 50: ICS Scalability: Expansion Example
First Response
Expanded

## Slide 51: Resource Definition & Classes
Resources: definition. All personnel and major items of equipment (including crews) that are available, or potentially available, for assignment to incidents. Resources are defined by Kind (function, e.g., a patrol car or bulldozer) and Type (performance, e.g. capacity or pressure factor)
Single Resources. Individual pieces of equipment and its personnel complement—or a crew of individuals with an identified supervisor—that can be used in a tactical application at an incident (e.g. a Medevac SH-60 Blackhawk helicopter)
Task Force. A combination of single resources assembled for a particular operational need, with common communications and a leader. Task Forces may be a mix of different kinds of resources.
Strike Team. Strike Teams are resources of the same kind and type (e.g., three drug K-9 teams, six patrol units, etc.). . Strike Teams must have a leader and communications among the single resources that make up the Strike Team—and between the Strike Team and its leader.

## Slide 52: Resource Status
Assigned resources are performing active functions.
Available resources are ready for immediate assignment.
Out-of-service resources are not ready for assigned or available status. Reasons for out-of-service include:
  Mechanical servicing required for vehicles and equipment.
  Personnel requiring a rest period, thus reducing personnel levels below an operational threshold.
  Environmental reasons, such as weather or darkness.
  Cost reasons—the cost of using the resource is prohibitive.

## Slide 53: ICS Facility Classes
Incident Command Post. The location at which the primary command functions take place. The Incident Commander is located at the ICP.
Base. The location at which primary logistics functions for an incident are coordinated and administered. There is only one Base per incident. (Incident name or other designator will be added to the term Base.) The Incident Command Post may be colocated with the Base.
Staging Area. Locations set up at an incident where resources can be placed while awaiting a tactical assignment. Staging Areas are managed by the Operations Section.
Camp. A geographic site, within the general incident area, separate from the Incident Base, equipped and staffed to provide food, water, and sleeping and sanitary facilities to incident personnel. In wildland fire application of ICS, Base activities may be performed at a Camp.
Helibase. Location in and around an incident area at which helicopters may be parked, maintained, fueled, and equipped for incident operations. Very complex incidents may multiple helibases.
Casualty Collection Points (CCP). Areas designated to receive, conduct triage, and provide treatment and transportation to individuals who have been injured at the incident. When CCPs are required, they may be divided into smaller areas to address receiving, triage, treatment, and transportation.

## Slide 54: ICS Order of Battle Model for Green/Blue Tank Scenario
Incident Command
Operations Section
Combat Ops Branch
Southern Division
Reconnaissance Group
Northern Division
4th Infantry Battle Group
FR Armor Strike Team 14
USA Task Force 1-70
Blue Tank
Green Tank
Disaster Relief Branch
Law Enforcement Branch
Planning Section
Fin/Admin Section
Logistics Section
Geographic
Functional
Major
Functional
Individual
Resource

## Slide 55: Multi-level Network Model for Green/Blue Tank Scenario
Green Tank
Blue Tank
Coalition Liaison
Wireless InterNet
(FM3TR+ALE)
Coalition
Router
Northern
Router
Southern
Router
North Cbt Ops
Wireless InterNet
FM3TR+ALE
South Cbt Ops
Wireless InterNet
FM3TR+ALE
Multiple
Connections Possible

## Slide 56: Example: Liaison Net Link Establishment
Green Tank
Blue Tank
Coalition Liaison
Wireless InterNet
(FM3TR+ALE)
Coalition
Router
Northern
Router
Southern
Router
North Cbt Ops
Wireless InterNet
FM3TR+ALE
South Cbt Ops
Wireless InterNet
FM3TR+ALE

## Slide 57: Example: Combat Ops Net Link Establishment
Green Tank
Blue Tank
Coalition Liaison
Wireless InterNet
(FM3TR+ALE)
Coalition
Router
Northern
Router
Southern
Router
North Cbt Ops
Wireless InterNet
FM3TR+ALE
South Cbt Ops
Wireless InterNet
FM3TR+ALE

## Slide 58: Cross-Domain Registration: Data Elements for Networking
A priori data elements
*Liaison net frequency scan list
*Liaison net TRANSEC code
*Liaison net COMSEC code
*Liaison net IFF code
*Liaison net (guest) ID for temp net access
Discovery data elements
*Unique ID
Nationality
Type
Kind
Subordination (OB)
Status
*Priority
*Clearance
Additional network data
* Mandatory elements