## Slide 1: Achieving Coalition C2 Interoperability Through Software Defined Radios
January 10, 2002 Sponsored by OSD (AT&L) IO SA
Modified 11/18/03

## Slide 2: Challenges
The flexibility inherent of software defined radio may be the enabler for true military coalition C2 tactical interoperability.
Commercial and/or military products must coalesce around an agreed upon set of standards and interfaces if individual national systems are to be interoperable.
Multiple commercial and military standards committees address only portions of the interoperability challenge.
Our task is to understand how such standards will integrate into a cohesive communications system to deliver interoperability and how you can validate with respect to standards.
We need Proof of Concept systems that converge US JTRS, UK Bowman/PDRS and other important national players’ systems.

## Slide 3: Methodology
Learn by creating a releasable, reference, open source, proof-of-concept and demonstration.
Demonstrate a US JTRS radio user discovering and communicating with a node in an independent radio network (as may be deployed by a coalition partner).
Populate the proof-of-concept team with experts drawn from both real world radio developers, military operators and standards activities.
Verify that a system built from this collection of standards is interoperable and practical to integrate and deploy.

## Slide 4: Four Communities
Coalition tactical command & control
Software radio infrastructure
Waveform implementation
Standards and acquisition management/policy bodies

## Slide 5: We Have A Lot of Commonality
Framework (SCA, C4ISR)
Waveforms (FM3TR, Link-22, …)
Components
Primitives
…

## Slide 6: Strawman Scenario
Consider an American tank that sees a coalition partner’s tank on a nearby hill. The tanks are likely on distinct nation-oriented defense networks. How does the American tank crew use a radio to spontaneously invite the coalition tank crew to lunch?
Sure, which bunker and what time?
Would you like to meet for lunch?

## Slide 7: Strawman Elements
6. Content (lunch? – voice, data, video)
2. Discovery (linking) waveform
5. Communications waveform(s)
4. Networking protocols
3. Identification process
1. C4I information (registry database)
Need a coalition waveform demonstration, incorporating elements that will leverage standards, communication, networking and modeling investments

## Slide 8: 1. C4I Database
Basic information is required before the communications negotiation begins
  Sender’s identification information
  Security parameters
  Waveform parameters
This information comes from the C4I system
  The sending tank might already have this information stored locally; or
  The sending tank might issue a real-time query into the C4I network.
Standards for how to transfer command and control parameters for SDR required – investigate ICS derivative
Notes: Radio problem is no longer just a radio technology problem. We need to know something of the information environment and a priori info that surrounds radios

## Slide 9: Why ICS (Incident Command System)?
Proven, efficient method used since 1990s including 9-11 disaster response
Designed for use by multiple agency types and echelons
  Unified command/control
  Federal, State, Local, NGOs
  Civil and military
  Ability to leverage commercial standards, devices & infrastructure
Well documented, open source information on interfaces, behavior, forms
  http://www.fema.gov/emi/is195.htm
  Easy to model
  Information available to all countries and organizations
Highly scalable
  Early response
  Expansion/Contraction
  Demobilization
Greater acceptance by the international community
  Widespread reluctance to adopt existing US military C4I models (many issues)
  More likely to draw widespread support in many parts of the world because of focus on emergency response
Extensible to coalition warfare
Ideal for homeland defense

## Slide 10: 2. Linking Waveform
In a hostile signals environment some parameters cannot be known in advance.
The receiving tank must discover the sending tank’s unexpected attempt to initiate dialog.
Existing standards in this domain include ALE for HF.
We have identified no discovery/link waveform examples in WDL or in C that conform to the SCA model.
Notes: Radios can shift their parameters almost instantly and go from an optimized configuration for just establishing the link to a configuration for secure and efficient bulk information transfer

## Slide 11: Linking Waveform Summary
Modify existing linking protocol stack from MIL-STD-188-141 (HF-ALE)
Use FM3TR (or Link-22) physical layer for VHF-UHF (CPFSK)
Mature HF-ALE software radio implementations are available as code sources (RL/IFGA), but not SCA. Can we re-use and re-deploy?
Can be used as a proposed link establishment method for nets in future US-NATO dialog
Sender
Xmits
Send IFF interrogation, encrypted Link (ID) over all freqs
Receiver listens
For ID
For each valid receipt, send IFF response, ID, signal strength
Sender selects best channel based on ID & signal strength

## Slide 12: 3. Identification Process
A process is required to identify the intended recipient by:
  Geographic location,
  Call sign,
  Type/kind,
  By-product of an IFF subsystem,
  Etc.
ID process involves interaction with the C4I system and emits parameters used by the linking waveform.

## Slide 13: 4. Networking Protocols
Strawman uses a TCP/IP stack to “simulate” whatever wireless IP protocol ultimately emerges.
Future over-the-air demo could substitute streamlined, wireless, defense-oriented version of IP.

## Slide 14: 5. Communications Waveform
We proposed FM3TR. Link-22 may be better choice now. ALE derivative will be inserted at FM3TR MAC layer using separate waveforms for discovery and communication.
Mercury has leveraged code base from successful US-UK-GE FM3TR (demo) to develop SE spec set and SCA-compliant waveform implementation.
Sound Capture and stream
Sound Reproduction
FM3TR Waveform Generation
Waveform Acq. and Data recovery
Frequency hopping Modulator
Frequency hopping Demodulator
Up Converter
Down Converter
T/R Switch
CVSD Vocoder
CVSD Vocoder
Multimedia H/W
Posix
Posix
Programmable Card
Channel simulation / RF Hardware
MIC
Speaker
Initial Prototype Module implementations
Future Enhancements
CORBA, SCA
CORBA, SCA

## Slide 15: FM3TR Summary
Future Multiband Multimode Modular Tactical Radio – “to ensure interoperability of software radios”
  Multi-national digital communications waveform
  Real-time, digital, frequency hopping
  AFRL has C code for CPUs &
  VHDL for FPGAs
Investigate availability &
applicability of AFRL WDL
waveform & process for
FM3TR (see backup)
FM3TR enhancements
for real world
Frequency Range
30-400 MHz
250 Hops/sec
Type
CPFSK
Rate
25 kb/sec
Index
0.5
Tx Spurious Emission

-75 dBm
Rx Image Rejection

-80 dBm
10 mW Tx
Power
Performance
Specification
Modulation
Hop Rate

## Slide 16: Green Tank, Blue Tank Communication
1. Shared a priori to engagement (mandatory):
  Frequency Scan List
  Communications waveform (e.g. FM3TR)
  ALE-derivative protocol
  IFF transponder code
  Network access and transmission security code
  Coalition ID code
  Coalition order of battle (OB)
Caller
Receiver
2/3. Discovery based interrogations (optional):
  Coalition OB information (Echelon/nationality, task force or strike team assignment)
  Resource capability summary
  Mission objective, clearance and priority
6. Inquiry (mandatory):
  Would you like to meet for lunch?
“Would you like to meet for lunch?”
2/3. Discovery based interrogations (mandatory):
  Identity based on Coalition ID code OR IFF transponder code and correct location/time

## Slide 17: Green Tank, Blue Tank Messaging
Secure automatic linking call + IFF interrogation
Secure automatic linking response + IFF reply
Discovery: I am a US Abrams attached to TF Green at [location]
Discovery: I am a French Leopard attached to Strike Team Blue at [location]
Inquiry: Would you like to meet for lunch?
Reply: Yes, your bunker or mine? Do you like quiche?
Reply: Your bunker is fine. Real tank crews don’t eat quiche.
Reply: Stand by for coded instructions for passage of lines
through our defensive screen using code X-ray…
Reply: Ready to decode X-ray
Coded transmission: Passage of lines information

## Slide 18: Strawman Functional Diagram
US Tank
Coalition Tank
Command & Control Functionality
IP Network
Channel
Simulation
Channel
Simulation
Comm.
waveform
Linking
waveform
SCA Core Framework
C4I Database
User
Interface
Comm.
waveform
Linking
waveform
SCA Core Framework
Foreign C4I Database
User
Interface
Notes: Only need small amount of C2 data
We will focus our attention on interfaces and behaviors and consulting
POC will not be a real working C2 system

## Slide 19: Waveform Development Environments
Communication service and protocol in waveform textual descriptions
Foresight’s or Racal’s WDL, Vanu’s RDL, or network layer functions in SIMULINK/MATLAB
Not MDA or SCA compliant.
Commercial
Ptolemy,
SystemView,
Foresight,
COSSAP,
GEDAE,
ISI,
SPW,
UML CASE
…
C4ISR
CADM,
DAFT,
JCAPS,
MRT,
CMMS,
JMAAT
…
Gudaitis/
Hinman

## Slide 20: Modeling Issues
Convergence of C4ISR Framework & AF C2 Enterprise Reference Architecture w/UML & SCA
  C2 nodes connected by CII Enterprise vs SDR node CORBA SW bus
  C4ISR Framework includes process model
  C4ISR Zachman-based Framework includes domain mandatory views
    Drill 4 dimensions of arch integration (National, Theater, CJTF, Tactical) and 3 architectural perspectives (operational, systems and technical)
  But not OMG standard (not UML or SCA)
Agreement on command & control model and network architecture, e.g., ICS
Alignment of evolving platform independent software radio behavior and platform specific models and WDL tools & library standards

## Slide 21: Summary
A coalition interoperability demonstration is needed, performing discovery, ID and communication over independent networks.
The effort should leverage standards, communication, networking and modeling investments, “give-back” to currently involved standards communities and consult to new C4I communities.
Must map to broad applications e.g. emergency broadcast and data casting (see backup), terrorism and natural disaster recovery, etc.
Serve to prove multi-national interoperability concepts.

## Slide 22: Backup Material

## Slide 23: ICS Overview (DRAFT) An Open-Architecture, Scalable Command and Control Model for Multi-Agency Joint Civil/Military Operations
http://www.fema.gov/emi/is195.htm

## Slide 24: Incident Command System (ICS) Candidate C4I Model can be extended to accommodate homeland defense and multi-national coalition operations
Command & control model in use by FEMA, FBI, DoD, states and local emergency response agencies
Designed for efficiency and scalability (early response, expansion, contraction, demobilization)
Used since 1990’s for disaster relief, firefighting, HAZMAT cleanup, search & rescue
Designed for multi-agency C3 including joint civil and military operations.
Well-suited for scalable, multi-national coalition operations
Incident Command
Operations Section
Combat Ops Branch
Southern Division
Reconnaissance Group
Northern Division
Main Battle Group
FR Armor Strike Team 14
USA Task Force 1-70
Blue Tank
Green Tank
Disaster Relief Branch
Law Enforcement Branch
Planning Section
Fin/Admin Section
Logistics Section

## Slide 25: ICS Scalable Command Function
The ICS Command Function provides a unified command structure, and can employ the most highly qualified individuals and resources from participating agencies.
The ICS permits ad-hoc formation of a command and control kernel during first response, scales gracefully as additional agencies and their resources join the organization, and offers excellent procedures for scale-down and demobilization.
First Response
ICS Command Function
“Full-up” Incident Response
ICS Command Function

## Slide 26: ICS Scalability: Expansion Example
First Response
Expanded

## Slide 27: Resource Definition & Classes
Resources: definition. All personnel and major items of equipment (including crews) that are available, or potentially available, for assignment to incidents. Resources are defined by Kind (function, e.g., a patrol car or bulldozer) and Type (performance, e.g. capacity or pressure factor)
Single Resources. Individual pieces of equipment and its personnel complement—or a crew of individuals with an identified supervisor—that can be used in a tactical application at an incident (e.g. a Medevac SH-60 Blackhawk helicopter)
Task Force. A combination of single resources assembled for a particular operational need, with common communications and a leader. Task Forces may be a mix of different kinds of resources.
Strike Team. Strike Teams are resources of the same kind and type (e.g., three drug K-9 teams, six patrol units, etc.). . Strike Teams must have a leader and communications among the single resources that make up the Strike Team—and between the Strike Team and its leader.

## Slide 28: Resource Status
Assigned resources are performing active functions.
Available resources are ready for immediate assignment.
Out-of-service resources are not ready for assigned or available status. Reasons for out-of-service include:
  Mechanical servicing required for vehicles and equipment.
  Personnel requiring a rest period, thus reducing personnel levels below an operational threshold.
  Environmental reasons, such as weather or darkness.
  Cost reasons—the cost of using the resource is prohibitive.

## Slide 29: ICS Facility Classes
Incident Command Post. The location at which the primary command functions take place. The Incident Commander is located at the ICP.
Base. The location at which primary logistics functions for an incident are coordinated and administered. There is only one Base per incident. (Incident name or other designator will be added to the term Base.) The Incident Command Post may be colocated with the Base.
Staging Area. Locations set up at an incident where resources can be placed while awaiting a tactical assignment. Staging Areas are managed by the Operations Section.
Camp. A geographic site, within the general incident area, separate from the Incident Base, equipped and staffed to provide food, water, and sleeping and sanitary facilities to incident personnel. In wildland fire application of ICS, Base activities may be performed at a Camp.
Helibase. Location in and around an incident area at which helicopters may be parked, maintained, fueled, and equipped for incident operations. Very complex incidents may multiple helibases.
Casualty Collection Points (CCP). Areas designated to receive, conduct triage, and provide treatment and transportation to individuals who have been injured at the incident. When CCPs are required, they may be divided into smaller areas to address receiving, triage, treatment, and transportation.

## Slide 30: ICS Order of Battle Model for Green/Blue Tank Scenario
Incident Command
Operations Section
Combat Ops Branch
Southern Division
Reconnaissance Group
Northern Division
4th Infantry Battle Group
FR Armor Strike Team 14
USA Task Force 1-70
Blue Tank
Green Tank
Disaster Relief Branch
Law Enforcement Branch
Planning Section
Fin/Admin Section
Logistics Section
Geographic
Functional
Major
Functional
Individual
Resource

## Slide 31: Multi-level Network Model for Green/Blue Tank Scenario
Green Tank
Blue Tank
Coalition Liaison
Wireless InterNet
(FM3TR+ALE)
Coalition
Router
Northern
Router
Southern
Router
North Cbt Ops
Wireless InterNet
FM3TR+ALE
South Cbt Ops
Wireless InterNet
FM3TR+ALE
Multiple
Connections Possible

## Slide 32: Example: Liaison Net Link Establishment
Green Tank
Blue Tank
Coalition Liaison
Wireless InterNet
(FM3TR+ALE)
Coalition
Router
Northern
Router
Southern
Router
North Cbt Ops
Wireless InterNet
FM3TR+ALE
South Cbt Ops
Wireless InterNet
FM3TR+ALE

## Slide 33: Example: Combat Ops Net Link Establishment
Green Tank
Blue Tank
Coalition Liaison
Wireless InterNet
(FM3TR+ALE)
Coalition
Router
Northern
Router
Southern
Router
North Cbt Ops
Wireless InterNet
FM3TR+ALE
South Cbt Ops
Wireless InterNet
FM3TR+ALE

## Slide 34: Cross-Domain Registration: Data Elements for Networking
A priori data elements
*Liaison net frequency scan list
*Liaison net TRANSEC code
*Liaison net COMSEC code
*Liaison net IFF code
*Liaison net (guest) ID for temp net access
Discovery data elements
*Unique ID
Nationality
Type
Kind
Subordination (OB)
Status
*Priority
*Clearance
Additional network data
* Mandatory elements